## Slide 1
M.TECH THESIS DEFENSE
Design and Verification of a Lightweight RISC-V-Based IoT Security Processor with Iterative Hardware-Reusable AES 128
Varada Inamdar | MIS 712438020
Guide: Dr. Ashwini Kulkarni
VLSI Design · Department of Electronics and Telecommunication Engineering
COEP Technological University, Pune | 2024–26
Iterative AES research → processor integration → end-to-end secure telemetry

## Slide 2
MOTIVATION
Why edge security is difficult
COEP Technological University
M.Tech Thesis Defense
02
Vehicle telemetry needs protection under tight area, power, and timing budgets.
!
SECURITY PRESSURE
SENSOR
IMU · speed
RAW DATA
visible on link
READ
REPLAY
ALTER
One false or exposed record can affect trust in downstream decisions.
µ
EDGE CONSTRAINTS
A
AREA
small FPGA / ASIC
P
POWER
limited activity
T
TIME
real-time response
Security cannot consume the resources needed by the sensing task.
DESIGN NEED
Hardware security with controlled area and activity

## Slide 3
CONTRIBUTION
One research path, three engineering layers
COEP Technological University
M.Tech Thesis Defense
03
01
Reusable AES-128
One round datapath reused for 10 rounds
02
RISC-V integration
MMIO + custom ISA + sensor/UART/DMA
03
Layered verification
Directed + random + UVM + Full-SoC
Research paper
M.Tech thesis system
Evidence and reproducibility

## Slide 4
THREAT MODEL
Security scope: what is protected, and what is not
COEP Technological University
M.Tech Thesis Defense
04
Implemented now
AES-CTR confidentiality Unique counter progression Hardware/software observability
Production additions
Authentication / integrity Replay protection Protected key storage Side-channel hardening

## Slide 5
CRYPTOGRAPHY
AES-128 primitive, CTR for streaming records
COEP Technological University
M.Tech Thesis Defense
05
Kᵢ = AESₖ(N ∥ CTRᵢ)
Cᵢ = Pᵢ ⊕ Kᵢ
✓
Same primitive
encrypt + decrypt
✓
No padding
record friendly
✓
Parallelizable
independent blocks
ECB retained only for NIST compatibility

## Slide 6
AES MICROARCHITECTURE
Why iterative hardware reuse?
COEP Technological University
M.Tech Thesis Defense
06
Proposed balance
1×
round datapath
10
controlled rounds
Tradeoff
Lower area and activity for higher block latency

## Slide 7
CADENCE GENUS · 55 NM · AES ONLY
Standalone AES: the reuse benefit is measurable
COEP Technological University
M.Tech Thesis Defense
07
96.77%
fewer cells
83,352 → 2,694
94.17%
lower cell area
202,949.64 → 11,841.48 µm²
96.10%
lower total power
21.9 → 0.853 mW
+6.806 ns
setup slack at 10 ns
critical data path 3.102 ns

## Slide 8
SYSTEM ARCHITECTURE
From cryptographic block to security processor
COEP Technological University
M.Tech Thesis Defense
08

## Slide 9
RISC-V INTEGRATION
The MEM stage becomes the internal security interconnect
COEP Technological University
M.Tech Thesis Defense
09
Address windows
0x300
AES / CTR
0x400
Sensor / SPI
0x500
UART
0x600
Interrupts
0x700
DMA-lite
0x800
Power

## Slide 10
CUSTOM-0 OPCODE
Custom security ISA: lower software control overhead
COEP Technological University
M.Tech Thesis Defense
10
0001011
RISC-V custom-0 opcode
CSEC_XOR
AES_STATUS
AES_START
AES_CT0
AES_CLEAR
MMIO remains available

## Slide 11
AUTONOMOUS VEHICLE SCENARIO
One 128-bit vehicle record, protected end to end
COEP Technological University
M.Tech Thesis Defense
11
1
Read sensor / SPI
2
Stage record with DMA
3
Encrypt using AES-CTR
4
Transmit ciphertext
5
IRQ → counters → sleep
Receiver regenerates keystream and XORs

## Slide 12
VERIFICATION METHODOLOGY
Verification grows from primitive to application
COEP Technological University
M.Tech Thesis Defense
12
1
AES KAT
NIST primitive correctness
2
CPU directed
RV32I-style behavior
3
Peripheral directed
MMIO + custom commands
4
Random smoke
changing values and addresses
5
UVM + C-DPI
independent reference model
6
Coverage
114 planned bins
7
Full-SoC
sensor → UART → sleep
Confidence increases with integration

## Slide 13
UVM ARCHITECTURE
Independent reference, serial monitor, end-to-end scoreboard
COEP Technological University
M.Tech Thesis Defense
13

## Slide 14
QUESTA WAVEFORM
Known-answer test: round-by-round correctness
COEP Technological University
M.Tech Thesis Defense
14
Key 000102…0E0F
Plaintext 001122…EEFF
10 rounds observed
Ciphertext 69C4E0…C55A ✓

## Slide 15
QUESTA FULL-SOC WAVEFORM
The complete transaction executes as one scenario
COEP Technological University
M.Tech Thesis Defense
15
Sensor read
DMA complete
AES-CTR done
UART output
IRQ + sleep

## Slide 16
REGRESSION SUMMARY
Verification closure: multiple proofs, one consistent result
COEP Technological University
M.Tech Thesis Defense
16
107 / 0
integrated RTL checks PASS / FAIL
CPU + AES + peripherals + scenario
100
random UVM transactions PASS
RTL vs C-DPI + UART
114
planned coverage bins
portable collector
7
verification layers
primitive to Full-SoC

## Slide 17
QUARTUS 23.1 · CYCLONE V · COMPLETE SOC
Integrated FPGA result: fits and meets 50 MHz timing
COEP Technological University
M.Tech Thesis Defense
17
13,257
ALMs · 23%
11,154
registers
+2.577 ns
worst setup slack
519.72 mW
vectorless estimate
low confidence
No DSP · no block RAM · no timing violations

## Slide 18
QUARTUS NETLIST EVIDENCE
Synthesis retains the complete integration hierarchy
COEP Technological University
M.Tech Thesis Defense
18
MEM: RAM + MMIO + peripherals
EX: forwarding + ALU + branch

## Slide 19
CADENCE GENUS · GPDK045 HVT · COMPLETE SOC
Complete SoC HVT synthesis: timing met at the slow corner
COEP Technological University
M.Tech Thesis Defense
19
50,968
mapped leaf cells
135,947.6 µm²
cell area · pre-layout
+2.315 ns
setup slack at 50 MHz
1.43753 mW
vectorless total power
synthesis-stage estimate

## Slide 20
CADENCE GENUS NETLIST
Technology-mapped view of the complete security processor
COEP Technological University
M.Tech Thesis Defense
20
50,968
mapped HVT leaf cells
17
retained hierarchies
HVT
GPDK045 mapped cells
Structural evidence not a placed layout

## Slide 21
INTERPRETATION DISCIPLINE
Three result domains answer three different questions
COEP Technological University
M.Tech Thesis Defense
21
AES only
Cadence Genus TSMC 55 nm RVT
Does reuse reduce AES area and power?
2,694 cells 0.853 mW
FPGA SoC
Quartus 23.1 Cyclone V
Does the integrated RTL fit and meet timing?
13,257 ALMs +2.577 ns
ASIC-style SoC
Cadence Genus GPDK045 HVT
How does the complete SoC map to HVT cells?
50,968 cells +2.315 ns
Do not compare unlike technology, scope, activity, or implementation stages.

## Slide 22
ENGINEERING INTERPRETATION
Low power is architectural first, physical later
COEP Technological University
M.Tech Thesis Defense
22
Pdyn = α · C · V² · f
What this RTL reduces
• duplicated AES round logic
• simultaneous active transformations
• CPU software-encryption workload
• idle peripheral activity through enables
What still needs physical evidence
Activity-based power
VCD / SAIF from real workloads
Clock-tree effects
post-CTS switching and insertion delay
Parasitics
post-route timing and power
Voltage corners
multi-mode, multi-corner sign-off

## Slide 23
LIMITATIONS AND QUALIFICATION
From thesis prototype to automotive deployment
COEP Technological University
M.Tech Thesis Defense
23
Production qualification: authenticated communication · secure provisioning · fault handling · ISO 26262 · ISO/SAE 21434

## Slide 24
CONCLUSION
What this thesis contributes
COEP Technological University
M.Tech Thesis Defense
24
01
Reusable AES
Large standalone area and power reduction
02
Complete SoC
CPU + AES-CTR + I/O + DMA + power
03
Two control paths
MMIO and custom security ISA
04
End-to-end proof
RTL ↔ C reference ↔ UART ↔ decrypt
05
Implementation evidence
Questa + Quartus + Genus
A publishable AES microarchitecture becomes a verified, thesis-ready security processor.

## Slide 25
THANK YOU
Questions and Discussion
Iterative AES-128 · Five-stage RISC-V · AES-CTR · Custom ISA · UVM · FPGA/ASIC evidence
Varada Inamdar | MIS 712438020
COEP Technological University, Pune
Design verified from sensor input to encrypted UART output and reference-model recovery